Static analysis of beam using refined 1D beam models

A cantilever beam having a square cross-section of edge length equal to 0.2m and length 2m made of isotropic material with E = 75 GPa and ν = 0.33. The structure is loaded by a vertical force equal to −50 N at the centre of the free tip (0,L,0) in the negative Z-direction. (Taken form the book - Finite Element Analysis of Structures through Unified Formulation by Professor carrera)

Lagrange polynomials have been taken for finding the cross sectional displacement field (X,Z)

Linear,quadratic and cubic elements have been taken for discretization across the beam axis(Y)

At first the problem has been solved using 1L4 element across the cross section and this produced promising results

After that the problem has been solved by discretizing the cross section using 2L4 polynomials

The stiffness matrix is found to be promising(I have checked it manually by deriving some of the components)

So the problem might arise from the loading vector that I have derived

In this mail I have attached the pdf image showing how I derived the load vector for both 1L4 and 2L4 elements across the cross section. And I have also attached the zip file containing the program that I have done using Python.