Static analysis of beam using refined 1D beam models

A cantilever beam having a square cross-section of edge length equal to 0.2m and length 2m made of isotropic material with E = 75 GPa and ν = 0.33. The structure is loaded by a vertical force equal to −50 N at the centre of the free tip (0,L,0) in the negative Z-direction. (Taken from the book - Finite Element Analysis of Structures through Unified Formulation by Professor Carrera)

Lagrange polynomials have been used for finding the cross sectional displacement field (X,Z)

Linear and quadratic elements have been taken for discretization across the beam axis(Y)

The problem has been solved using 1L4 element across the cross section.